## Slide 1: Using ERT to enter a Semiannual Visible Emission Observation Major and Area Source Foundry NESHAPs
PART OF A HOW-TO SERIES FOR USING ERT AND CEDRI
FOR SEMIANNUAL VE AND COMPLIANCE REPORTING

## Slide 2
Verify you have Microsoft Access version 2010 or up
If you do not have Microsoft Access:
You will need to download and install the runtime version of Microsoft Access from the Microsoft Access Download Center. A link to the download center is provided on the EPA ERT website. Please download a version that is the version of office you have installed on your computer.
• MS Access 2010 Runtime.
• MS Access 2013 Runtime.
• MS Access 2016 Runtime.
• After installing the Runtime version of Microsoft Access, follow the instructions below to install and run the ERT.

## Slide 3
Downloading and Installing the ERT
The EPA Electronic Reporting Tool (ERT) Webpage contains the latest versions of the ERT, the spreadsheet templates, the user’s guide, and example data sets.
Once you’ve determined that you are running a version of MS Access which is capable of running the ERT Application, follow these two steps.
Download the latest version of the program application. This file includes the latest version of the ERT and the user's guide.
2. To run the ERT, right click on the downloaded zip file and select “Open”. Select a destination for the extracted files. Go to the destination folder and double click on ERTv6.accdb file. It is recommended that the ERT program file and the data set files be located on a local drive (i.e.. C: or desktop). Some functionality of the ERT is lost across servers or external drivers.
To start the ERT, double click ERTv6.accdb file from the location where you’ve installed the ERT application.
Depending on how your version of Access is configured, you may see a “Security Warning” window (as shown below) when you try to start the ERT.

## Slide 4
1. Following installation launch the database
2. Select - Stop All Macros and the red X in the upper right-hand corner of the Macro Single Step box

## Slide 5
Select - Enable Content
(it is possible you may not see this screen)

## Slide 6
Select - Continue

## Slide 7
Select -> Create New Project Data Set (PDS)

## Slide 8
Enter a Project Data Set File Name
For example -> M22SemiannualJune2021
Select -> Create New Project Data Set
NOTE: The first time you create a project data set you have to do the above steps. Thereafter you can select the above project data set and click on “Save Project Data Set As” to save the entire PDS with another name or save only the test plan part of the first data set as a template.
First browse for the location of the folder to store the Project Data Set or maintain the provided and identified default folder.
There have been reported issues with moving the folder so suggest leaving the Project Data Set Folder where it was created.

## Slide 9
Select -> Select Project Data Set
A browse menu will appear to allow you to select the project data.

## Slide 10
Select the PDS from the default folder and click “Open”

## Slide 11
Save Project Data Set As
Source tests for similar sources may contain some of the same information. To keep from having to enter the same information for similar tests, the ERT can save the currently selected PDS as a template. When this happens, a new PDS is created with the current test plan information saved and all the other data deleted. However, the attachments are not deleted and will need to be removed. The new template PDS can then is used as a starting point for a similar source test. The ERT also can save all of current PDS data into a new PDS.

## Slide 12
Select -> Yes

## Slide 13
Enter name for your template and select “OK”

## Slide 14
If working with a new Project Data Set you will only be able to access the Setup/Test Plan Menu
Select -> Test Plan

## Slide 15
Complete all red asterisk data fields
Complete all red asterisk data fields
NOTE AFTER DISCUSSIONS WITH USEPA
I COMPLETED MANY NON-ASTERISK
FIELDS. ON THE FOLLOWING SLIDES
YOU MAY CHOOSE TO DECREASE SOME
DATA ENTRY, AS LONG AS MEANINGFUL
INFORMATION IS RETAINED.
After completing move to the next
section by clicking “Next Page”

## Slide 16
Select -> Select SCC from list

## Slide 17
Select these levels which will then populate “30400399”
Select “/hr” from the Select Time Unit drop down menu then select “OK”

## Slide 18
After selecting “OK” from the previous screen this popup appears.
Following discussions with USEPA these were the suggested selections or entries.
After completing select “OK”

## Slide 19
Select -> Next Page

## Slide 20
Select -> Add Location

## Slide 21
Enter a name for the VE Location
Select -> Save and Exit

## Slide 22
Select -> “Add Target Parameters”

## Slide 23
From Select Location Drop Down Menu ->
Select the Location you Entered
From the Select Method Drop Down Menu ->
Select “Custom”
Note: Method 22 will not appear until later.

## Slide 24
After selecting “Custom” this popup menu appears. Complete and select -> Close and Save
USEPA has indicated they plan on including Method 9 and possibly Method 22 in future releases of ERT.

## Slide 25
Enter “Number of Test Runs” and “Test Run Duration”

## Slide 26
Check the “Select from All Compounds” box
Select “Custom” from the Drop Down Menu
Select this Leader

## Slide 27
After selecting the leader in the previous slide this popup box opens.
Complete the required entries and Select -> Close and Save

## Slide 28
Select -> “Save Selected Items”

## Slide 29
Select -> Add Emissions/Concentrations

## Slide 30
This Popup will appear.
Select Location from the Drop Down Menu
Whether using a M-9 or M-22 select > percent(%) from the Available menu and move it over by selecting the leader.
Select -> Save Selected Items

## Slide 31
Select Next Page

## Slide 32
Check the “Part 63 (MACT)” box
Enter a description of the test
Select -> Add Regulation

## Slide 33
Select Part 63 Subpart EEEEE if a Major Source
or
Select Part 63 Subpart ZZZZZ if an Area Source of HAPs
Select “Visible Emissions” from the Drop Down Menu
Select “Save and Exit”

## Slide 34
If test will not be used for other than NESHAP compliance enter “No”; otherwise enter “Yes” and explain
Select -> Next Page

## Slide 35
Select -> Add Control Device
Select -> Add Process

## Slide 36
Select Location from Drop Down Menu
Select “UNCONTROLLED” from the Drop Down Menu
Select -> Save and Exit

## Slide 37
Select -> Next Page

## Slide 38
Select -> Next Page
The “next page” the audit calibration is not shown in this slide deck. Just select “Next Page”

## Slide 39
Select -> Next Page
This language is Area Source specific language. It is possible that major sources need to provide a 30-day notification prior to a VE
test.

## Slide 41
Select -> Finished
Select the paperclip and select and attach test results.

## Slide 42
To create a submission file, click “Create ERT Submission Package File.” If any required fields are not complete, a window will open with a list of links to the screens. Click on the links to the screens to complete the fields. Once the field window is closed, click on the “Re-Check Data” button. When all the required fields have been completed, the “Create ERT Submission File” window will open as shown on next slide.

## Slide 43
Select ->>> “1” and the next screen will appear

## Slide 44
Click on “Continue” button to skip this process and continue to create the submission package file.

## Slide 47
Select 2 and complete if you only if you would like.
Select 3
An action window will appear with instructions as it creates the ERT Submission file, a PDS zip file and an ERT Submission zip file. When the “Finished” is clicked, the location of the field will be reported in the field.